## Slide 1
GroundTruther
From plugin to measurement instrument
A QGIS plugin for seafloor characterization — multibeam acoustics, seafloor
imagery, survey video and now stereo geometry, together on one map.
Development update · September 2026 · v0.4 · QGIS 4 / Qt 6

## Slide 2
Recap — what it is
• Runs inside QGIS as a dock-based toolset
• Joins four data worlds on one map:
  – MBES bathymetry + backscatter (ARA)
  – Seafloor imagery (HabCam-style stereo stills)
  – Survey video with per-frame GPS
  – Stereo geometry — micro-DEMs, roughness, mosaics (new)
• Ground-truth annotation → statistics → KMZ / HTML reports
• Heavy work stays server-side: GRASS backend + a GPU stereo service
🖼 Screenshot
GroundTruther docked in QGIS (overview)

## Slide 3
Where it stands today
when | what landed
Apr 2026 | Port to QGIS 4 / Qt 6, Python 3.14, dock UI, video player
Jun 2026 | FastGIS authenticated GRASS API · session persistence · stereo roughness, micro-DEM 3-D and georeferenced mosaics
Sep 2026 | Config hardening · full docs site · the 180° georeference fix · the photogrammetric seabed ribbon
in parallel | HRS1508 — a frozen-manifest analysis asking whether stereo roughness actually adds to acoustics
Act I — the engineering that made the tool trustworthy · Act II — the new optical-geometry tools · Act III — the first science they made possible.

## Slide 4
Act I
The platform
QGIS 4 / Qt 6 · docks & sessions · configuration · internals ·
FastGIS · query builder · video · reports · docs

## Slide 5
QGIS 4 / Qt 6 support
PLATFORM
• Full port to QGIS 4.0+ / Qt 6 (system Python 3.14)
• Qt 6 API rework: scoped enums, exec_ → exec
• Fixed Qt 6 dock-walk crashes — register docks with the QGIS main window,
  – never with the plugin's inner QMainWindow
• OpenGL 3-D viewer made Qt 6-safe (PyOpenGL context)
• QWebEngineView → QTextBrowser (WebEngine absent from QGIS 4 OSGeo4W)
• Wayland: launch QT_QPA_PLATFORM=xcb for floating docks
• qgisMinimumVersion = 4.0
🖼 Screenshot
plugin running in QGIS 4 (toolbar + docks)

## Slide 6
Dock workspace & session persistence
GUI
• Each tool an independent dockable / floatable panel: image browser, video
  – player, query builder, report builder, GRASS tools, seafloor roughness
• 'Restore default layout' + reliable save/restore of docked layout
• Session persistence: a groundtruther_project file
• Restores image index, zoom, query selection, dock layout, map-sync
• Written on QGIS project save · loaded at start → resume where you left off
🖼 Screenshot
custom dock layout + Settings (session file field)

## Slide 7
Configuration that degrades instead of failing
ROBUSTNESS
• The old model was all-or-nothing: one stale path and the plugin would not start
• 27 keys, validated per key and severity-aware; pydantic v2 is the schema of record
• Only the two image paths are errors — everything else is a warning when
  – set-but-invalid, and silent when unset
• degrade() blanks only the failed keys → a bad value disables its own feature
• Config values treated as untrusted throughout
• Settings dialog covers every key and saves by merging into the file on disk
  – (the old fixed template silently deleted whole sections)
• Cloud panels hide themselves when no service is configured
🖼 Screenshot
Settings dialog + a validation report in the message log

## Slide 8
Internals — modular, tested, documented
INTERNALS
• Thin orchestrator + focused mixins — dockwidget ≈ 240 lines:
  – image browser · video browser · video annotation · GRASS · roughness ·
  – report · settings · layout · session
• Stateless, testable core (gt/) — no Qt, unit-tested:
  – grass_api · image_manager · video_manager · task_runner · mbes_fields ·
  – session_state · roughness_client / _geo / _dem / _spectrum / _interpret · ribbon
• 415 tests collected (unit / GUI-offscreen / integration) — including tests that
  – guard the conventions: import hygiene, settings-docs drift, UI-built-once
• Non-trivial work is planned first in PLANNING/, executed in a dedicated git
  – worktree, and closed out with a progress log

## Slide 9
FastGIS — the GRASS backend
API
• Legacy flat, unauthenticated endpoint → api.fastgis.eu
• Authenticated (X-API-Key), built around an environment model (env_id)
• Schema-driven module dialogs — any GRASS module rendered from its interface
  – description; async runs polled via a QgsTask
• Detachable QGIS panel: module picker, push output rasters back into QGIS,
  – show/hide the computational region
• Same credentials carry the stereo roughness service
🖼 Screenshot
GRASS Tools panel + a generated module form

## Slide 10
MBES query builder & ARA
FEATURE
• Draw a sampling unit (ellipse / rectangle) on the soundings
• ARA scatterplot, 3-D surface, histograms, statistics, in-shape image selection
• Multi-level backscatter: auto-detects every BSWG-2015 level present
  – (BS_raw → BS_RL → BS_TL → BS_area → BS_AVG), back-compatible
• Beam-side filtering (Raw / Port / Starboard / Fold) works correctly
• Sampling centre uses the calibrated USBL fix, so marker, sample and
  – georeferenced rasters all coincide
🖼 Screenshot
query builder: sampling unit + ARA scatterplot

## Slide 11
Video player
FEATURE
• Frame-accurate player docked in QGIS, driven from the metadata track
• Interlaced-source support: PyAV + yadif — fixes the FFmpeg-8 black-frame failure
• Geo-link: the canvas follows the frame at a fixed, CRS-independent map scale;
  – marker and map stay in sync during play
• GPS track persisted as a real GeoJSON layer — restored with the project,
  – auto-regenerated on load
• Per-frame bounding-box annotation; loads the MAREANO .log format directly
🖼 Screenshot
video dock + GPS track on the map

## Slide 12
Reporting
FEATURE
• One click sends query-builder products to the report builder: ARA scatterplot,
  – 3-D surface, histogram, statistics, sampling-unit description, image gallery
• Output to KMZ (geo-referenced balloon) and a templated HTML report (Jinja2):
  – card layout, uniform thumbnails, click-to-zoom lightbox, browsable gallery
• PDF export of the composed report
🖼 Screenshot
HTML report with gallery + statistics table

## Slide 13
Documentation
DOCS
• User-facing docs are a MkDocs Material site, published to
  – epifanio.github.io/groundtruther on merge
• Installation (Linux / macOS / Windows) · Tools (one page per feature) ·
  – Configuration (all 27 keys + the validation model) · Data model · Architecture
• A data-model reference documents every column the plugin reads — including
  – which position column is the USBL fix and which is a model.
  – This is what surfaced the 180° bug in Act II.
• mkdocs build --strict in CI catches broken links and orphan pages; a unit test
  – fails if a config key is added without its documentation row

## Slide 14
Act II
Optical geometry
Stereo reconstruction · roughness · georeferencing · mosaics ·
the seabed ribbon

## Slide 15
The gap this act is about
Roughness is measured inside one camera frame. Backscatter is measured over a footprint metres across. Between them sat a scale range nothing was measuring.
product | wavelengths it supports
per-frame stereo micro-DEM | ~3 mm … 1.2 m (one frame's footprint)
MBES bathymetry (1 m grid) | ≥ 2–3 m
the photogrammetric ribbon | 3 mm … 170 m — it spans the whole range
γ₂ is fitted at frame scale, then used to interpret acoustics at metre scale. Nobody had checked the power law holds across the gap.

## Slide 16
Stereo photogrammetric reconstruction
NEW TOOL
• A real-height micro-DEM of the patch under the camera, from the HabCam
  – stereo pair itself — independently of the acoustics
• Computed server-side on a GPU (RAFT-Stereo, SGBM fallback). Only the frame's
  – Imagename is sent — no image bytes leave the machine
• Float32 heights in millimetres, ~2–5 mm cells, NaN no-data, plus a
  – cell-for-cell co-registered orthophoto
• Micro-DEM 3-D tab — the mesh draped with the orthophoto 1:1 (one texel/vertex)
• Edge spikes masked, not hidden: trim border · clip σ · erode
• Background QgsTask, cached per frame: ~14 s first, ~0.5 s after
🖼 Screenshot
Micro-DEM 3D tab, photo-textured mesh

## Slide 17
Seafloor roughness — γ₂, and what to trust
NEW TOOL
• Metrics tab: γ₂ · substrate & texture hints · w₂ · rms height · rugosity ·
  – anisotropy · altitude · quality · matcher
• Spectrum tab: radial relief power spectrum log-log, fitted power law, fit band
  – shaded, γ₂ / w₂ / R² annotated
• γ₂ — the spectral exponent — is the load-bearing output. Robust across matchers
• w₂ and rms are NOT trustworthy in absolute terms: no consistent RAFT-vs-SGBM
  – bias, and the median rms (50 mm) sits far above the 3–23 mm literature range
• When quality != ok, every field is null — shown, not faked
• Where the curve peels off the fit at high K, that's the stereo noise floor
🖼 Screenshot
Metrics + Spectrum tabs side by side

## Slide 18
Georeferencing — and a 180° bug worth telling
FIX
The bug (#31): the plugin sent the nav's `bearing` column as heading. bearing points ASTERN — so every georeferenced product was rotated 180°, and a saved ±180 heading offset was the natural way to paper over it.
hypothesis | median residual | within 30°
heading = bearing (old) | −175.3° | 0 %
heading = bearing + 180 | +3.9° | 100 %
• Proved on the imagery, not by argument: imagery-derived course minus nav course
  – over 250 registered frame pairs (table above)
• Side benefit: a single frame's heading is good to ~4° — now a measured number
• Rotation ≠ reflection. Heading offset fixes a rotation; Mirror fixes a handedness
  – flip. No rotation can undo a reflection — rasters exported before the fix
  – are 180° out and need regenerating

## Slide 19
Georeferenced mosaics
NEW TOOL
mode | how frames are placed
Auto (default) | Per window, from nav-predicted overlap: piled-up → pixel, well-spread → flat
Flat | Navigation alone (position, heading, flat-seabed scale). Fast
Ortho | Relief-corrected per-frame orthophoto, then nav placement. Slowest
Pixel | Registered by image content, georeferenced through the reference frame's nav
• Illumination correction (flat-fields the strobe vignette) and gain compensation
  – on by default — this is what makes a mosaic look continuous
• Presets: Browse (3 mm, fast) · Publication (ortho, 0.8 mm, lanczos, 8192 px, RGBA)
• Honest failure mode: featureless mud cannot be content-registered by any method —
  – 'only 0/10 pairs registered — low texture, mosaic is nav-placed'

## Slide 20
The photogrammetric seabed ribbon
NEW
• Composite a few hundred per-frame micro-DEMs along ONE HabCam line into ~170 m
  – of millimetre-resolution georeferenced seabed. A script (scripts/build_ribbon.py),
  – not yet a dock — look at a ribbon first
• Choose the strip by TEXTURE, never by relief. On this survey they are
  – uncorrelated: two runs with ~4 m of relief (3.75 and 4.04 m) linked on 0 % of
  – sampled pairs — featureless mud — while the strip with the MOST relief in the
  – survey (5.80 m) managed only 22 median inliers. Picking by relief would have
  – chosen one of the dead ones
• ORB + RANSAC needs help here: no preprocessing (CLAHE and flat-fielding both
  – LOWERED inliers), a loose Lowe ratio 0.95, detection masked to the overlapping
  – band, and a displacement prefilter + physical gate — without the gate RANSAC
  – confidently returns 15–25-inlier consensuses on completely wrong transforms
• Pixels where they work, navigation everywhere else: the USBL is
  – piecewise-constant (median step 92 mm against a true 491 mm), so nav-placed
  – frames stack in clumps of ~6 and jump. The chain integrates the links, bridges
  – gaps with nav, then rubber-sheets back onto it — absolute placement from the
  – USBL, relative geometry from the pixels

## Slide 21
The ribbon — measured
RESULTS
Strip 6663–6958: 296 frames, 172 m, EPSG:32619, track-aligned at 273.1°, 1256 × 48 339 cells at 3 mm.
link rate | 89.8 % (265 / 295 pairs), median 309 inliers
longest unbroken registered run | 119 pairs (mean 48)
quality != ok | 2.0 % (6 frames, all insufficient_coverage)
service altitude vs Altimeter | median 37 mm
seam error, pixel-linked | 62.0 mm → 13.7 mm after levelling
seam error, nav-bridged | 235.5 mm → 119.3 mm — 8.7× worse
• The vertical error was the depth sensor, not the stereo. V_Depth is quantized to
  – 10 mm and steps with σ = 82 mm — essentially the whole per-frame scatter.
  – Levelling solves per-frame offsets from overlap medians (robust IRLS, lag-1 and
  – lag-2 pairs for loop closure), keeping the datum with the vehicle
• The trade, stated: seams 4.5× better, but the 1 m profile agrees LESS with the
  – MBES (0.147 → 0.185 m). Some large corrections over-fit bad overlaps
• Independent checks: chain azimuth 273.1° vs nav 273.2°; focal length calibrated
  – against nav displacement 2507 px vs nominal 2480.28 — ratio 1.011

## Slide 22
Does the power law cross the gap?
SUGGESTIVE, NOT SETTLED
• The per-frame fit is 2-D and isotropic; a ribbon profile measures the 1-D
  – spectrum. Integrating out the cross-track wavenumber gives a closed form with
  – NO free parameter — so γ₁ = γ₂ − 1 and the amplitude are both predicted
• Measured in the 1.2–3 m band: 9.45× (+9.8 dB) more power than the per-frame law
  – predicts, fitted γ₁ = 2.29 ± 1.56 against a predicted 1.97
• The slope is unconstrained. ±1.56 spans every plausible exponent — the band is a
  – third of a decade, all a 145 m ribbon can offer
• The amplitude excess is only 1.7× above the ribbon's own noise floor: a per-frame
  – vertical error held across each frame and changing every 0.49 m puts a nearly
  – FLAT spectrum across exactly this band (14× at the robust σ = 21 mm)
• What would settle it is now a number: per-frame vertical placement must reach
  – ≈ 6 mm, from 60 mm — a vertical bundle adjustment
• Supporting: MBES along-track γ₁ = 3.60 ± 0.16 (γ₂ ≈ 4.60) over 2–40 m, far
  – steeper than the per-frame 2.97, with the ribbon's 3.29 BETWEEN them — the shape
  – of a gradual break, at an error bar that makes it a remark
• And the ribbon does not beat the altimeter on vertical accuracy (0.185 m vs
  – 0.115 m median |dz| against the MBES). It adds texture, not depth

## Slide 23
Act III
The science it made possible
HRS1508 — does stereo roughness add anything to acoustics?

## Slide 24
HRS1508 — the question and the setup
Does optical roughness carry substrate information that backscatter does not? A binary problem — Substrate A vs Substrate E — on the HRS1508 survey.
stream | what went in
MBES beams | 29 027 174 beams, all 512 formed beams/ping, full angular range
cells | 25 m grid → 2318 ARA cells (median 9846 beams/cell, 6 angle bins)
optical nav | 123 394 HabCam frames, positioned by calibrated USBL
stereo roughness | 12 563 per-frame records → γ₂, rugosity, anisotropy
analysis set | 217 cells with a majority single-substrate label and ≥ 3 roughness frames
• 7 ARA descriptors (6 × 10° angle bins + slope), per-line normalised so the
  – unknown source level cancels, plus 3 roughness features
• Random forest, 5-fold spatially blocked CV on 200 m blocks (33 blocks); folds
  – frozen once and reused, so every comparison is genuinely paired

## Slide 25
The result
HEADLINE
model | accuracy | gain vs ARA | 95 % CI
ARA only (baseline) | 0.659 | — | —
ARA + γ₂ | 0.691 | +0.032 | −0.005 … 0.072
ARA + γ₂ + rugosity | 0.714 | +0.055 | 0.005 … 0.108
ARA + all roughness | 0.756 | +0.097 | 0.039 … 0.155
roughness only | 0.756 | +0.097 | 0.014 … 0.183
• Block-permutation p < 0.001; macro-F₁ 0.597 → 0.715; minority-class (Substrate E)
  – recall 0.43 → 0.60 — the gain is where it matters
• γ₂ ranks FIRST of all ten features (importance 0.215, above every backscatter
  – bin — the best of those is 0.175)
• Modality ladder: backscatter alone 0.70 · + bathymetric slope correction 0.66 ·
  – + γ₂ 0.69 · + all roughness 0.76
• Holds across scale: at a 15 m cell the same ladder runs 0.74 → 0.83
• Two-tier map: 881 of 2318 cells (38 %) have both modalities; adding roughness
  – flips 14.5 % of the classified swath

## Slide 26
Why you can believe it — and what it does not say
• One run, one manifest. Two earlier fusion results (0.769→0.864 on 221 cells,
  – 0.761→0.820 on 987 cells) differed in BOTH the beam table and the cell subset —
  – invisible to the author, obvious to a referee. The fix was not to pick a number,
  – it was to make two impossible: one frozen manifest.yml, one library, one beam
  – table, one fold assignment, every input hashed into a lock file
• Calibration stress test: inject per-line source-level error up to 5 dB (against a
  – MEASURED per-line spread of 4.59 dB over 17 lines). The normalised pipeline moves
  – 0.000; without per-line normalisation it drifts 0.018; strip the shape too and the
  – level-only classifier falls to 0.58 and drifts 0.028. The result does not depend
  – on absolute calibration
• The image classifier survives honest CV: 0.942 stratified → 0.939 on 200 m
  – spatial blocks. Optimism 0.002 — it was not leaking geography
• LIMITS, stated not buried — the stereo coverage gate is NOT label-neutral:
  – 2.7 % of Substrate A cells rejected against 12.9 % of Substrate E (Fisher OR 5.3,
  – p ≈ 2×10⁻²⁵). That is a result about turbidity over fine sediment
• w₂ and rms height are never model inputs — amplitude is not recoverable from
  – this stereo; and fit_r2 / valid_fraction / altitude_mm / matcher are absent from
  – the committed CSVs, so spectrum quality cannot yet be filtered on

## Slide 27
Is this a unique tool?
• Yes — and the differentiator has shifted
• It started as an INTEGRATION argument: most workflows are siloed — acoustics in
  – one suite, image annotation in another, video review in a third, GIS somewhere
  – else. GroundTruther puts them on one QGIS map, free and open source
• It is now also a MEASUREMENT argument: no other GIS-native tool turns the
  – survey's own stereo imagery into metric seabed geometry — micro-DEMs, spectral
  – roughness, georeferenced mosaics, a millimetre ribbon — and puts it beside the
  – acoustics in the same project
• Heavy work stays server-side (FastGIS for GRASS, a GPU service for stereo);
  – the plugin stays a thin, scriptable client
• Open formats throughout (Parquet, GeoJSON, GeoTIFF, KMZ, CSV/.log)
• Not a replacement for specialist acoustic suites — a connective, ground-truthing
  – layer, which now measures something of its own

## Slide 28
What's next?
Committed, with a number attached
• Vertical bundle adjustment for the ribbon: per-frame placement 60 mm → ≈ 6 mm. That single factor of ten converts the scale-gap result from suggestive to publishable
• Persist the roughness QC fields (fit_r2, valid_fraction, altitude_mm, matcher) so spectrum quality can be reported and filtered on
• Resolve mount handedness against a target of known handedness — the one link in the geometry chain still untested
Open
• ML-assisted annotation (review instead of draw)
• A ribbon dock in QGIS, once people have used a ribbon in anger
• Multi-line ribbons and cross-line closure
• Reproducible 'analysis as a saved session'
• Multi-user / shared cloud sessions; signed report bundles
• More survey-log adapters; CI toward a turnkey installer

## Slide 29
Would you use it?
Who it's for
• Benthic ecologists & seabed-mapping teams doing ground-truthing
• Anyone who wants acoustics, imagery and video on the same map without stitching five tools together
• New: anyone who needs quantitative seabed geometry from imagery they already have — without building a photogrammetry pipeline
Honest take
• Purely acoustic processing → keep your specialist suite
• Sub-metre optical geometry at survey scale with full bundle adjustment → this is not a photogrammetry suite (yet)
• Interpretation + ground-truth + reporting across data types, inside GIS, open and scriptable → yes, and the optical side now measures as well as displays

## Slide 30
Need help setting it up?
• Requirements: QGIS 4.0+ (Qt 6), the bundled .venv, a FastGIS API key for GRASS
  – and roughness (or a direct URL if you run the GPU service yourself)
• Install: symlink the repo into your QGIS profile, enable, point Settings at your
  – data — invalid keys now disable only their own feature
• Try it: the Zenodo 'groundtruther test dataset' (CC-BY-4.0)
• Repo & issues: github.com/epifanio/groundtruther
• Docs: epifanio.github.io/groundtruther · dev notes in docs/grass_fastgis.md
  – and docs/photogrammetric_ribbon.md
• Analysis workflow: PDAL_MBIO/paper — frozen manifest, notebooks 00→09
• Happy to walk you through install, config, or your own dataset.

## Slide 31
Thank you
GroundTruther · v0.4 · QGIS 4 / Qt 6
MBES · imagery · video · stereo geometry · roughness · mosaics · ribbon · report
github.com/epifanio/groundtruther · epifanio.github.io/groundtruther